## Slide 1
NOBEL WEIGHING SYSTEMS
Solutions for Crane Weighing
Notes: Presentation of Nobel Weighing Systems a part of VPG

## Slide 2
Advantages of Nobel Crane Weighing
Custom designed load cell makes solution easy to implement
Multiple load cell applications can be managed by one instrument.
Instrument provides “level supervision” of all load cells for intelligent weighing
Specially developed software for crane weighing
  Setup & Display functions for Crane applications
  Life Cycle datalogger automatically calculates “working life” of crane
  Mean value measurement for accurate weighing under dynamic loading

## Slide 3
Crane Weighing
Weighing (process, inventory control)
Overload Control
Load imbalance
Life Cycle (optimize service & maintenance intervals)
Accurate Crane weighing with custom made load cells located in
  Lower Block
  Upper Block – Equalizing Sheave

## Slide 4
Crane weighing application
KIMD load cells in crane trolley weighing entire bridge crane

## Slide 5
Rope Tension Transducer, “clamp on wire” when load cells can’t be installed.
RTT
Less Accurate Crane weighing with rope tension transducer
Overload application
Accuracy 2 % R.O., Repeatability 1% R.O
Wires up to 1-1/2 in (36 mm) diameter
Dead weight calibration necessary

## Slide 6
Load Cells for Offshore Cranes
200kN to 2 MN (45k to 450k LB)
Built-in transmitter 4-20 mA
Dual bridge and transmitters
Hazardous location approval
Accuracy of load cell
  0,1 to 1% (customer demand)
Load Cells used
  KOSD
  KIMD
  KISD
Applications
  Weighing
  Overload
Specifications

## Slide 7
Mooring and Chain Stoppers
Specifications
4-12 MN (450k to 2700k LB)
Built-in transmitter 4-20 mA
Dual bridge and transmitters
Hazardous location approval
On deck or submerged
  Material
  IP Class
Accuracy of load cell
  < 1% (customer demand)
Load Cells used
  KOSD

## Slide 8
Transmitter for Offshore Applications
Analog output 4-20 mA
Supply voltage ±10-30 VDC
Hazardous location approval
IP 68 and IP69K (Submerged)
Features

## Slide 9
Load Cell models
KISD-type
KIMD-type
KOSD-type

## Slide 10
KISD-6
Highest accuracy 0,1%
50, 100, 200, 400, 1000 kN
(11k, 22k, 45k, 90k, 225k lbs)

## Slide 11
KIMD
Medium accuracy 0,25%
500, 800 kN
(112k, 180k lbs)

## Slide 12
KOSD-40, -101, -107, -115
Less accurate (0,5 to 1%) than KISD/KIMD but is lower cost
KOSD-40
  10,20, 50, 100, 200 500 kN
  (2.25k, 4.5k, 11k, 22k 112k lbs.)
KOSD-101, 107 1000 kN (225k lbs)
KOSD-115 2000 kN (450k lbs)

## Slide 13
Large and Small load cells:
Capacities 100 lb – 660 ton
Diameter ½ in – 15 in
Length 2 in – 80 in
KISD, KIMD, KOSD
Custom Load Cells

## Slide 14
Generation 3 Instruments
8,300,000 Count Total Resolution
Dynamic Digital Filtering
High speed analog output (300 updates/second)
Modbus RTU protocol
Profibus DP available WST 3
Hazardous locations AST 3IS
+/- 10 VDC, 0-20 or 4-20 mA Isolated Analog output
Relay output standard
Data sheet (electronic) or dead weight Calibration
PC software (deltaCOM) for setup & configuration
Features
AST 3P/3B
AST 3IS
WST 3

## Slide 15
Generation 4 Instruments
Multi-channel (synchronous measurement)
Modular hardware design (flexible and configurable)
High speed input (800 updates/second)
Flexible measurement output via FUNCTION BLOCKS
Software upgrades easily downloaded
Remote diagnostics and monitoring (web interface)
Custom Application software easily developed
Features
G4 Panel Mount
G4 Rail Mount